Simple Finite State Machine Example
W. Dobson 5-14-2018

The following represents the FSM implemented in the example code for assignment #3. It uses boolean inputs: visible and inrange to control the state transitions. Where visible means that this character can see the player and inrange means that the player has gotten too close causing the character to flee the situation. Although not in this implementation you may want to add a timer that used to extend/delay state transitions so the the character continues to flee for a while after the threat is removed.

        State Bubble Diagram

State Transition Table
Present State	Transition Rules	Next State
IDLE	player not visible	IDLE
IDLE	player visible	ALERT
ALERT	player visible and not inrange	ALERT
ALERT	player visible and inrange	FLEE
ALERT	player not visible	IDLE
FLEE	player visible and inrange	FLEE
FLEE	player not visible or not inrange	ALERT

Note that typically the number of input variables (n) can control up to 2n states. So for 2 inputs it can control up to 22 = 4 states which is sufficient for the 3 states in this machine example.